## Slide 1: MCQ DENTURE BASE RESIN

## Slide 2
1) In heat cure denture base resins the monomer is
a) methacrylate
b) ethylmethacrylate
c) metyl ethyl methacrylate
d) polymethylmethacrylate

## Slide 3
2)If curing occurs at temperature more than 100 degree celsius porosity results in which are of denture
a)hard thick central area
b) thin palatal area
c)thin area of flanges
d) porosity is uniformly distributed

## Slide 4
3)What is the shrinkage if 3:1 powder:liquid ratio is used
a) 6%
b) 8%
c) 10%
d) 21%

## Slide 5
4) Hydroquinone is added to methyl methacrylate monomer
a) to prevent polymerization during storage
b)to initiate release of free radicles
c) to enable polymerisation reaction at room temperature
d)all of the above

## Slide 6
5) cross linking of denture base is contributed by
a)gylcol dimethacrylate
b) benzoyl peroxide
c) N para toluidine
d) methyl methacrylate

## Slide 7
6) use of dimethyl P toluidine is indicated for
a) thermal polymerization of acrylic
b) chemical polymerization
c) retarding the polymerizing reaction
d) to inhibit the action of benzoyl peroxide

## Slide 8
7)Porosity present in acrylic denture is usually the result of
a) prolonged curing cycle
b) lack of sufficient pressure applied to flask
c) insufficient acrylic resin monomer
d) prolonged bench cooling after curing

## Slide 9
8)The most important disadvantage of acrylic denture base is
a) porosity
b)shrinkage
c)tooth breakage
d)water absorption

## Slide 10
9)In self cure acrylic resin the activator is
a) toluidine
b) quaternary ammonium compound
c) benzoyl peroxide
d) tertiary amine

## Slide 11
10) Which of the following may result if an excessive amount of monomer is incorporated into an acrylic resin mixture
a) excessive expansion
b) low impact strength
c) excessive shrinkage
d) excessive brittleness